## Slide 2
Owner and CEO of the international consulting company TECSA S.r.l. (www.tecsasrl.it)
Vice President of the Italian Association of Fire Engineering (SFPE-Italy)
Chair of the Institute of Risk Management (UK) Italy Regional Interest Group
Principal engineer exida L.L.C. (USA)
Luca.Fiorentini@tecsasrl.it
Luca Fiorentini
PRESENTACIÓN - INTRODUCTION

## Slide 3
Lessons learnt from real cases
of risk assessment in ports area
L. Fiorentini
TECSA S.r.l. (Italy)

## Slide 4
Maritime transport is the backbone of the international trade and global economy. Around 80% of global trade by volume are carried by sea and are handled by ports worldwide (United Nations Conference on Trade and Development, UNCTAD, 2014)
Nowadays, the dependency of the EU and of developed countries on seaports for the trading of goods is very high. Imports and exports of goods to and from the rest of the world make up 75% of the trade, while intra-EU trade makes up 36%. In Europe, over 300 ports are active in ro-ro, general cargo, liquid bulk, and/or dry bulk handling, and about 130 seaports handle containers
The number of European ports handling containers is expected to increase in the following years.
In the EU, seaborne traffic represents 20% of the total transport. In 2015, EU ports handled around 3.8 billion tonnes, 1.3% more than in 2014. Rotterdam is the largest container port in Europe, with 11.6 million 20-foot equivalent units (TEUs) handled, followed by Antwerpen with 9.4 million TEUs and Hamburg with 8.8 millionTEUs
Marittime transport importance

## Slide 5
Categories of accidents (1996-2015)

## Slide 6
A disruption of any kind in the working of a seaport system has the capability to bring about disastrous and cataclysmic consequences.
The danger of calamitous accidents in a port environment is mainly associated with the presence of hazardous cargo.
The hazardous cargo under specific situations and vulnerabilities and at certain magnitudes can result in leaks, fires and at certin magnitudes can reult in leaks, releases, fire and explosions.
Ports must be resilient and be able to function as needed under both expected and unexpected conditions.
Disruption importance: safety/assets and business continuity (supply chain)

## Slide 7
Hazardous cargoes
In the shipping globalization context, the port construction of all countries in the world is in a period of rapid development.
As the global demand for petrochemical products soars, the hazardous cargo throughputs of global ports are also growing rapidly.
The varieties and quantities of flammable, explosive, corrosive, and toxic chemicals stored at ports are increasing day by day, and the hazardous cargo terminals and storage facilities are characterized by a large quantity, a wide distribution and an high risks.
These factors have led to increasing safety risks of port operations, and further led to frequent safety management accidents.
Therefore, it is imperative to control the hazardous cargo accidents at ports.

## Slide 8
Tianjin Port Accident (2015)
Tianjin Port caused serious casualties, property losses, environmental pollution and other negative impacts.
In terms of casualties and property losses, the accident caused 165 deaths, 8 missing and 798 injured and hospitalized, as well as damage to 304 buildings, 12,428 commercial automobiles and 7533 containers.
The accident caused the explosion, combustion, leakage and diffusion of at least 129 varieties of chemical substances. The explosion also ignited surrounding buildings and large quantities of ordinary goods such as cars and coke.

## Slide 9
According to the investigation report of the hazardous cargo explosion accident at Tianjin Port the causation factors of the explosion are primarily divided into four categories, namely,
environmental factors;
human factors;
management factors;
facility factors;
cargo factors.
Investigation

## Slide 10
Within the shipping industry, ports have a signiﬁcant role as they operate as the connection between sea and land, as well as with the hinterland, in order to be able to load and unload the transported products.
A port area is characterized by a wide range of activities: whereas some of these activities are common to the majority of industrial areas (e.g. big oil terminals, presence of rail and road traﬃc, chemical and petrochemical plants, general manufacturing and industry), there are several activities that are to be encountered exclusively in a harbour setting.
Aspects of navigation and ships: loading and unloading of goods, oil jetties, shipyards, the presence of ﬁshing ﬂeets, marinas, dredging, the building of port infrastructures, crowds for passengers, etc.
As a result, ports are complex organizations and source of potential risks of accidents due to the ship traﬃc and the multiple activities that are carried out there, including the significant growth in existing areas (congestion).
Port complexity
PORT
(including port in land terminals)
INTERFACES
TRAFFIC
SHIPS
at anchor

## Slide 11
Among these instigating factors, the human factors is considered as the most prominent that counts for a huge portion of the overall accidents in the hazardous cargo maritime transport sector,
Their result revealed that mental fatigue, lack of adequate training, and inadequate supervision ha a critical role in accident causation.
The human factor is highly diversified when it comes to the instigation of hazardous cargo and maritime accidents. It involves the qualification, experience, training, mental and psychological state, use and abuse authority, errors and violations, definition and implementation of safety measures, the developed rules and measures, followed and implemented technological and physiological setup and the organizational composition on the part of involved employees.
Human factors

## Slide 12
Human factors

## Slide 13
Safety culture

## Slide 14
Safety Management System applied to plant (Annex III)
Main pillars:
ORGANISATION AND PERSONNEL
IDENTIFICATION AND EVALUATION OF MAJOR HAZARDS
OPERATIONAL CONTROL
MANAGEMENT OF CHANGE
PLANNING FOR EMERGENCIES
MONITORING PERFORMANCE
AUDIT AND REVIEW
Very similar in structure to the
OSHA (USA) PSM model
EU Directive 2012/18/EU, 4 July 2012, “Seveso III”, Requirements
Notes: Two are the main provisions of the Seveso 3 directive: Safety Managemente Systems and the Safety Report.
It follows the OSHA (osha) https://www.osha.gov/Publications/osha3133.html Process Safety Management

## Slide 15: EU Directive 2012/18/EU, 4 July 2012, “Seveso III”, Requirements
Safety Report (risk assessment) (Annex III)
Minimum data and information to be considered:
IDENTIFICATION AND ACCIDENTAL RISK ANALISYSIS AND PREVENTION METHOD
MAJOR ACCIDENTS SCENARIOS AND THEIR PROBABILITY
CAUSES:
OPERATIONAL
EXTERNAL (DOMINO)
NATECH
CYBER
CONSEQUENCES
REVIEW OF PAST ACCIDENTS AND INCIDENTS (EVEN NEAR-MISSES)
TECHNICAL PARAMETERS AND EQUIPMENT (DCS, ESD, ALARMS, ...)
PROTECTION MEASURES
EMERGENCY PLAN
Notes: Consider all the new risk (i.e. Cybersacurty) DCS Ditribuited Control System, BPCS (Basic Process Control Systems)

## Slide 16: EU Directive 2012/18/EU, 4 July 2012, “Seveso III”, Requirements
ROLE of the AHJ
AHJ should VERIFY that the Risk Reducing Factors (RRFs) DECLARED in the Safety Report (by the Plant Owner) are valid and maintained during the life-cycle of the plant, by the support of the Safety Management System put in place.
Declared PFD shouldn’t exceed data used in the risk assessment.
Two different inspections:
On the Safety Report content (assumptions, results, risk mitigation plans);
On the Safety Management System (major accidents risk from the safety report is kept under control during time?).
Notes: Probability of Faliure on Demand

## Slide 17: EU Directive 2012/18/EU, 4 July 2012, “Seveso III”, Requirements
MAPP
adequate safety and reliability
Notes: Underline that from authority point of view we are much more interested in the DEMONTRATION (Combinational failure rate, verify the Risk reduction achoeved) TO MAKE SURE THEY ARE DOING THE RIGHT THING

## Slide 18: EU Directive 2012/18/EU, 4 July 2012, “Seveso III”, Requirements
Chart: Results of inspections in Italy (2016÷2019)
| 23% Organisation & Personnel - Competency | 7% Risk assessment - Lack in detail | 70% Operation
Results of inspections (2016÷2019) | 0.23 | 0.07 | 0.7
- Safety Critical Element management
- Test and Inspection
- Maintenance
- Documentation
- Management of change
Problems rise in OPERATION rather then in RISK ASSESSMENT
Real problem is: DEFENCE Vs OPERATION
Be aware: safety issues are also business continuity/reputation problems
Notes: Italian data of inspections. The safety management pillars, main problems are not risk assessment connected but more related to the management system! To manitaine the same level of safety!

## Slide 19: EU Directive 2012/18/EU, 4 July 2012, “Seveso III”, Requirements
MOC is a pillar of the Safety Management System.
AHJ should verify that MOC process is included and actuated for each plant modification and plant life-cycle coincides with the prevention / protection measures life-cycles.
Notes: !COINSIDES! To make sure thet the chagnes are assessed properly to evalute the impact in the overall safety of the plant.

## Slide 20: Safety Report & Safety Management System
Safety Management System
Plant modifications
Changes should be classified (maintenance, no risk increase, risk increase). MOC process should involve also fire protection systems: to be considered SCE (safety critical elements) too.
Fire safety
Specific Italian decree to consider fire safety measures in ”upper tier” Seveso Plants as SCE (as ESD, alarms, asset integrity, etc.).
Basic elements of the Safety Management System
Organization and staff;
Identification and evaluation of relevant hazards;
Operational control;
Changes and design;
Emergency planning;
Performance check;
Check and review.
Content required for the
safety report
Identification data and location of the plant;
Plant information;
Plant Safety;
Emergency situations and related preparations;
Waste treatment plants and waste storage;
Certifications and insurance measures.
Risk identification
Risk classification
Risk mitigation
Periodic risk monitoring and review
    MAIN STEPS OF RISK MANAGEMENT
Basic elements of the Safety Management System
RISK ANALYSIS
Content required for the Safety Report
Operator
Notes: Stringere un po’, Possibile Eliminazione

## Slide 21
A specific law (D.M. 293/2001), no more valid (Seveso II related):
Integrated port safety report for industrial ports (RISP):
  Risk assessment
  Procedures (to prevent) and Emergency Procedures (to mitigate)
  Coordinated: owners, third-parties, authorities
To be prepared by Port Authority and approved by a pool of AHJs
To be used for the Port Emergency Plan
Integrated Port Safety Report (RISP)

## Slide 22
“RISP” structure:
Integrated Port Safety Report (RISP)
A – Port and interfaces
B – Legislation (law, regulations)
C – Risk assessment
D – Emergency plan

## Slide 23
Risk assessment (frequency and consequences) should include:
accidents from Seveso plants (Safety Reports)
accidents during transfer operations between ship and land;
accidents during vehicle loading/unloading operations;
accidents during wagon loading/unloading operations railways.
possible domino effects also in relation to the transit/transfer of hazardous substances
recompositing of possible area hazards (including FN curves)
Risk assessment in RISP:

## Slide 24
Investigated ports
Venezia
Taranto
Augusta
Cagliari

## Slide 25
Port and interfaces
TERRITORIAL FRAMEWORK
Overview of the Port of Venice

## Slide 26
Port and interfaces
Port areas

## Slide 27
Port and interfaces
Companies list

## Slide 28
Port and interfaces

## Slide 29
Port and interfaces

## Slide 30
Port and interfaces

## Slide 31
Risk assessment

## Slide 32
Risk assessment

## Slide 33
Risk assessment

## Slide 34
Risk assessment

## Slide 35
Risk assessment

## Slide 36
Traffic risk assessment
Graphic recompositing of the naval traffic regulations in the Port of Taranto by virtue of the regulations in place prepared by the Port Authority.

## Slide 37
Traffic risk assessment
Traffic regulation in the Gulf of Cagliari, general overview

## Slide 38
Traffic risk assessment

## Slide 39
Traffic risk assessment
Routes and waypoints

## Slide 40
Traffic risk assessment

## Slide 41
Traffic risk assessment

## Slide 42
Real investigation (e.g. Tianjiin)

## Slide 44
Bow-Tie: proposed approach

## Slide 45
Bow-Tie: general structure

## Slide 46
Bow-Tie: simple notation to deal with HFs

## Slide 47
Bow-Tie: preventive measures

## Slide 48
Bow-Tie: protection measures

## Slide 49: Tool
https://www.chaosconsulting.it/en/cards/

## Slide 50: Holistic composition towards a maturity model
Training and competence
Maintenance
Work procedures
Time programming
Management system
Performance standards - Traditional audit Vs. Barrier based inspection
Training and competence
Maintenance
Work procedures
Time programming
Management system
PERFORMANCE BASED APPROACH
(ANALYSIS, DESIGN, OPERATION)
IT CAN INTEGRATE MORE RAGAGEPs IN A MATURITY MODEL
SINGLE-FOCUS APPROACH
MORE RESOURCES NEEDED, SPECIALIZED TEAMS DO NOT EXCHANGE INFORMATION
DIFFICULT TO IMPLEMENT AND MANTAIN
Notes: Not focused just on one safety aspect.

## Slide 51
Barrier based audit

## Slide 52
Active-Reactive

## Slide 53
Conclusions

## Slide 54
(Cyber)security
Energy transition
Terrorist attack
Emerging threaths